## Slide 1: Line Strengths and Self-Broadening of Pure Rotational Lines of Carbon Monoxide and Nitrous Oxide Measured by Terahertz Time-Domain Spectroscopy
Presentation to the 11th HITRAN Database Conference, 2010, Cambridge, MA, USA
16 June, 2010
Weston Aenchbacher1, Mira Naftaly2, and Richard Dudley2
1Currently with Drexel University, Department of Electrical and Computer Engineering, Philadelphia, PA, USA
2National Physical Laboratory, Hampton Road,Teddington, Middlesex TW11 0LW, UK

## Slide 2
Introduction
NPL terahertz time-domain spectrometer (THz-TDS)
CO Measurements and Results
  Pure rotational lines from J’ = 3 ← 2 to J’ = 22 ← 21
  Pressures of 0.7 – 5.1 bar
N2O Measurements and Results
  Pure rotational lines from J’ = 10 ← 9 to J’ = 53 ← 52
  Pressures of 0.7 – 1.2 bar

## Slide 3
NPL Terahertz Time-Domain Spectrometer
biased photoconductive emitter
ZnTe refractive index proportional to THz E-field → rotates probe polarization
Ti-sapphire laser
mode-locked
800 nm centre wavelength
20 fs pulse length
77 MHz repetition rate
THz emitter
biased GaAs
probe beam
pump beam
Wollaston
prism
ZnTe
electro-optic
crystal

## Slide 4
NPL Terahertz Time-Domain Spectrometer

## Slide 5
Time-Domain Measurement
probe pulse
THz pulse 20 ps
Probe pulse 2 fs →
~delta function

## Slide 6
THz Spectrum
E-field in time
Spectrum
FFT
GHz

## Slide 7: Sample CO Spectrum
(a)
(b)
(c)
Lorentzian line shape assumed
CO absorption spectrum at 2 bar
Section of sample fit at 2 bar
Expanded section of fit at 2 bar

## Slide 8
Line Center with Pressure, J’ = 9 line
J’ = 9 center frequency (minus HITRAN) vs. pressure
error bars → standard deviation

## Slide 9
Sample Measurements, J’ = 9 line
γself = slope
fit amplitude vs. pressure
fit linewidth vs. pressure
y error bars → standard deviation
x error bars → pressure uncertainty

## Slide 10
CO Line Center Frequencies
peak frequency (minus HITRAN) for J’
Peak frequencies are taken as average over all pressure measurements.

## Slide 11
CO Results
Line Intensity for J’
Self-Broadening coefficient for J’
Tabulated data can be found:
W. Aenchbacher, M. Naftaly, and R. Dudley, “Line strengths and self-broadening of pure rotational lines of carbon monoxide measured by terahertz time-domain spectroscopy,” Applied Optics 43/13, pp. 2490, 2010.
error bars → standard deviation
Notes: Add at bottom, reference and “tabulated data can be found…”

## Slide 12
Sample N2O Absorption Spectrum
(left) absorption spectrum at 1.2 bar
(right) section of sample fit at 1.2 bar

## Slide 13
N2O Sample Measurements, J’ = 29 line
(top) absorption fit amplitude vs. pressure
(bottom) fit linewidth vs. pressure
vertical 95% confidence bars, horizontal pressure uncertainty
zero point included to decrease fit uncertainty

## Slide 14
error bars → 95% confidence interval
center frequency (minus HITRAN) for J”
N2O Line Center Frequencies

## Slide 15
N2O Parameters Calculated
Parameter |  | This work | From literature
B | From line frequencies & Eq. 1 | 12.53 ± 0.08 GHz 0.418 ± 0.03 cm-1 | 0.419 cm-1 a,b
 | From line intensities & Eq. 2 | 12.3 ± 0.2 GHz 0.410 ± 0.008 cm-1 | 
Electric dipole moment 0 |  | –0.155±0.003 D | -0.161 D b,c
Eqn. 1
Eqn. 2
E.D. Palik, K.N. Rao, “Pure rotational spectra of CO, NO, and N2O between 100 and 600 microns”, J. Chem. Phys., 25/6 (1956) 1174-1176.
F. Rohart, J.-M. Colmont, G. Wlodarczak, J.-P. Bouanich, “N2- and O2-broadening coefficients and profiles for millimeter lines of 14N2O”, J. Mol. Spectr., 222 (2003) 159-171.
L. Nguyen, J. Buldyreva, J.-M. Colmont, F. Rohart, G. Wlodarczak, E.A. Alekseev, “Detailed provile analysis of millimeter 502 and 602 GHz N2O-N2(O2) lines at room temperature for collisional linewidth determination”, Mol. Phys., 104 (2006) 2701-2710.

## Slide 16
N2O Results
line intensity vs. J”
self-broadening coefficient vs. J”
Tabulated data available soon:
W. Aenchbacher, M. Naftaly, and R. Dudley, “Line strengths and self-broadening of pure rotational lines of nitrous oxide measured by terahertz time-domain spectroscopy,” JOSA B. (submitted May 2010).
error bars → 95% confidence interval

## Slide 17
Conclusion
THz TDS demonstrated as a viable tool for measurement of molecular spectra.
Contribution to knowledge base of CO molecule
  Measured intensity and self-broadening with THz-TDS for the first time
Contribution to knowledge base of N2O molecule
  Measurements to fill gaps in available experimental data for intensity and self-broadening

## Slide 18
Thank You
For more information:
W. Aenchbacher, M. Naftaly, and R. Dudley, “Line strengths and self-broadening of pure rotational lines of carbon monoxide measured by terahertz time-domain spectroscopy,” Applied Optics 43/13, pp. 2490, 2010.
W. Aenchbacher, M. Naftaly, and R. Dudley, “Line strengths and self-broadening of pure rotational lines of nitrous oxide measured by terahertz time-domain spectroscopy,” JOSA B. (submitted May 2010).
Weston Aenchbacher: wla24@drexel.edu
Mira Naftaly: mira.naftaly@npl.co.uk
Financial support for this work was provided by the National Measurement Office, an Executive Agency of the Department for Business, Innovation, and Skills. W. Aenchbacher was on the MSc, Photonics and Optoelectronic Devices Program of the University of St. Andrews

## Slide 19
NPL Terahertz Time-Domain Spectrometer
Ti-sapphire laser
mode-locked
800 nm centre wavelength
20 fs pulse length
77 MHz repetition rate
beam
splitter
probe
beam
pump beam
delay
stage
THz emitter
biased GaAs
balanced
photodiode
detector
Wollaston
prism
ZnTe
electro-optic
crystal
Gas Cell
THz
beam
parabolic
mirror
parabolic
mirror
parabolic
mirror
parabolic
mirror
biased photoconductive emitter
ZnTe refractive index proportional to THz E-field (Pockels Effect) → rotates probe polarization

## Slide 20
CO Tabulated Results
W. Aenchbacher, M. Naftaly, and R. Dudley, “Line strengths and self-broadening of pure rotational lines of carbon monoxide measured by terahertz time-domain spectroscopy,” Applied Optics 43/13, pp. 2490, 2010.
Notes: Ditch tables

## Slide 21
J’←J’’ | Line intensities (cm-1/molecule.cm-2) x 10-22 |  |  | J’←J’’ | Line intensities (cm-1/molecule.cm-2) x 10-22 |  | 
 | Measured |  | HITRAN (error not reported) |  | Measured |  | HITRAN (error not reported)
 | value | error |  |  | value | error | 
10←9 | 0.54 | 0.08 | 0.570 | 32←31 | 2.84 | 0.18 | 2.85
11←10 | 0.64 | 0.08 | 0.727 | 33←32 | 2.67 | 0.11 | 2.73
12←11 | 0.93 | 0.15 | 0.901 | 34←33 | 2.62 | 0.13 | 2.61
13←12 | 0.90 | 0.08 | 1.09 | 35←34 | 2.62 | 0.16 | 2.47
14←13 | 1.28 | 0.10 | 1.29 | 36←35 | 2.34 | 0.11 | 2.33
15←14 | 1.52 | 0.08 | 1.49 | 37←36 | 2.19 | 0.11 | 2.18
16←15 | 1.54 | 0.11 | 1.70 | 38←37 | 2.15 | 0.11 | 2.03
17←16 | 1.79 | 0.10 | 1.91 | 39←38 | 1.91 | 0.11 | 1.87
18←17 | 2.06 | 0.12 | 2.11 | 40←39 | 1.74 | 0.11 | 1.72
19←18 | 2.13 | 0.13 | 2.30 | 41←40 | 1.63 | 0.08 | 1.57
20←19 | 2.3 | 0.08 | 2.48 | 42←41 | 1.57 | 0.09 | 1.43
21←20 | 2.65 | 0.17 | 2.64 | 43←42 | 1.36 | 0.08 | 1.29
22←21 | 2.63 | 0.12 | 2.78 | 44←43 | 1.25 | 0.08 | 1.16
23←22 | 2.78 | 0.15 | 2.90 | 45←44 | 1.32 | 0.07 | 1.03
24←23 | 2.94 | 0.15 | 2.99 | 46←45 | 1.01 | 0.08 | 0.916
25←24 | 2.96 | 0.20 | 3.06 | 47←46 | 0.92 | 0.08 | 0.809
26←25 | 3.04 | 0.14 | 3.10 | 48←47 | 0.93 | 0.08 | 0.710
27←26 | 3.13 | 0.12 | 3.12 | 49←48 | 0.74 | 0.08 | 0.620
28←27 | 3.15 | 0.21 | 3.11 | 50←49 | 0.58 | 0.08 | 0.539
29←28 | 3.03 | 0.13 | 3.07 | 51←50 | 0.58 | 0.08 | 0.466
30←29 | 2.98 | 0.13 | 3.02 | 52←51 | 0.64 | 0.08 | 0.400
31←30 | 3.04 | 0.17 | 2.94 | 53←52 | 0.39 | 0.08 | 0.342
N2O Tabulated Results - Intensities

## Slide 22
J’←J’’ | Self-broadening (GHz/atm) |  |  | J’←J’’ | Self-broadening (GHz/atm) |  | 
 | Measured |  | HITRAN 2% error 5% |  | Measured |  | HITRAN 2% error 5%
 | value | error |  |  | value | error | 
10←9 | 3.1 | 0.3 | 3.24 | 32←31 | 2.7 | 0.1 | 2.61
11←10 | 2.7 | 0.6 | 3.21 | 33←32 | 2.5 | 0.1 | 2.61
12←11 | 3 | 0.4 | 3.18 | 34←33 | 2.6 | 0.1 | 2.58
13←12 | 2.5 | 0.5 | 3.12 | 35←34 | 2.7 | 0.1 | 2.58
14←13 | 3.1 | 0.2 | 3.09 | 36←35 | 2.5 | 0.1 | 2.55
15←14 | 2.8 | 0.2 | 3.06 | 37←36 | 2.6 | 0.1 | 2.55
16←15 | 2.8 | 0.2 | 3.03 | 38←37 | 2.6 | 0.1 | 2.52
17←16 | 2.8 | 0.2 | 2.30 | 39←38 | 2.8 | 0.1 | 2.52
18←17 | 3 | 0.2 | 2.97 | 40←39 | 2.5 | 0.1 | 2.49
19←18 | 2.8 | 0.2 | 2.94 | 41←40 | 2.6 | 0.1 | 2.49
20←19 | 2.6 | 0.1 | 2.91 | 42←41 | 2.6 | 0.1 | 2.49
21←20 | 2.9 | 0.2 | 2.88 | 43←42 | 2.6 | 0.1 | 2.46
22←21 | 2.6 | 0.1 | 2.85 | 44←43 | 2.6 | 0.3 | 2.46
23←22 | 2.8 | 0.1 | 2.82 | 45←44 | 3.1 | 0.3 | 2.43
24←23 | 2.8 | 0.2 | 2.79 | 46←45 | 2.6 | 0.4 | 2.43
25←24 | 2.8 | 0.1 | 2.78 | 47←46 | 2.8 | 0.5 | 2.43
26←25 | 2.7 | 0.1 | 2.76 | 48←47 | 3.4 | 0.3 | 2.40
27←26 | 2.7 | 0.1 | 2.73 | 49←48 | 2.5 | 0.2 | 2.40
28←27 | 2.8 | 0.1 | 2.70 | 50←49 | 2.7 | 0.4 | 2.40
29←28 | 2.6 | 0.1 | 2.67 | 51←50 | 2.7 | 0.5 | 2.37
30←29 | 2.7 | 0.1 | 2.67 | 52←51 | 3.4 | 1.1 | 2.37
31←30 | 2.8 | 0.1 | 2.64 | 53←52 | 2.3 | 0.4 | 2.37
N2O Tabulated Results – Self-Broadening

## Slide 23
Carbon Monoxide

## Slide 24
Line Parameters
where
L.S. Rothman, et al: The HITRAN molecular spectroscopic database and HAWKS (HITRAN atmospheric workstation): 1996 Edition, J. Quant. Spectrosc. Radiat. Transfer Vol. 60/5, 1999, pp 665-710.

## Slide 25
Measuring Line Parameters
Assume each line is a Lorentzian:
and assuming an ideal gas:
obtain A(P) by Lorentzian fits at various pressures